## Slide 1: Locally Non-rigid Registration for Mobile HDR Photography
Orazio Gallo, Alejandro Troccoli, Jun Hu, Kari Pulli, and Jan Kautz
Notes: Today I’m going to talk to you about registration for HDR imaging. This is work in collaboration with Alejandro Troccoli, Jun Hu, Kari Pulli, and Jan Kautz.
Before diving into the method, however, I would like to make sure we are all on the same page with what HDR is.

## Slide 2
http://www.flickr.com/photos/lprowler/5704117093/
what is HDR?
Notes: If you are an enthusiast photographer, you may be associating HDR with what I like to call “overly contrasted” pictures, as in this image. But there’s more to HDR than that.

## Slide 3
what is HDR?
Notes: This is an HDR image too. And I put it here it to show that HDR is not about how “contrasty” the final result looks, but rather about the DR, which is the ratio of the brightest and darkest points IN THE SCENE!

## Slide 4
World
log-luminance
(log cd/m2)
-2
4
8
-6
what is HDR?
Notes: It’s important to remember that our visual system is extremely advanced; its many adaptation mechanisms, distributed from the actual photoreceptors in our eyes, all the way through our visual pathways, allow us to perceive a starlit sky as well as the flash of a camera, despite the fact that one is 14 orders of magnitude larger than the other.
The DR a standard camera can capture is very limited, but we can simulate adaptation,
<CLICK>
by taking multiple shots of the same scene with different exposure times.

## Slide 5
what is HDR?
Notes: In fact, this is exactly how I captured the image I showed before
In order to merge differently exposed images, however, our stack needs to be aligned at the pixel level. Simply put, pixel i,j in one image in the stack must “see” the same part of the scene across the whole stack.

## Slide 6
Notes: To explain to you what happens when this assumption is violated, here is a stack I captured.
I wanted to take an HDR picture of my friend, but I was was taking too long...
<CLICK>
<CLICK>
So my friend got impatient and started moving...
<CLICK>…
and other things happened as well…
<CLICK>
... aaaaand now you get artifacts in your final picture
So registration, which is the process of aligning pixels in the different images, is really important. If we are not able to compensate for the displacement between images, we may introduce stronger artifacts than saturation or under-exposure.

## Slide 7
Quality
Speed
Rigid registration
(Ward ‘03,
Tomaszewska and Mantiuk ‘07, …)
Fully non-rigid registration
(Hu et al. ‘12, Sen et al. ‘12,
Hu et al. ‘13)
Rejection methods
(Gallo ‘09,
Zhang and Cham ‘12,
Oh et al. ‘15 …)
Flow-based methods
(Zimmer et al. ‘11,
Zhang and Cham ‘12,…)
Accelerated patch-based
(Bao et al. ‘14)
Related work
Minutes
Seconds
Milliseconds
No artifacts
Parallax
and
motion artifacts
Motion artifacts
or
reduced dynamic range
Notes: And indeed a lot of methods were proposed to address this problem.
There are extremely fast methods that don’t quite solve all the problems, and methods that work extremely well even in the presence of arbitrarily large displacements. But this comes at the cost of minutes on desktops for small images.
What I am going to show you today, is a method that works as well as the best methods <CLICK> but is as fast as the fastest methods.

## Slide 8: A sparse-to-dense approach
Compute the flow at sparse locations,
Propagate the flow in an edge-aware fashion, and
merge the images in an error-tolerant way.
Notes: To achieve this, we propose a…

## Slide 9
Reference
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Source
Notes: Let’s dive into our algorithm. We start from two of the images in the stack: a reference and a source. Our final goal will be to non-rigidly warp the source so that it looks geometrically identical to the reference, but with its original exposure level.
The first step of our algorithm is to find reliable matches between the two images, and of course we want this to be extremely fast and robust in the presence of exposure changes. The standard way of doing this is to find salient features in both images
<CLICK>
and match them.
<CLICK>
Having matches, is equivalent to having the flow at those locations, which in turn means that we can warp the images to each other.
We take a different route: we only look for features in the reference image.

## Slide 10
Reference
Source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: In particular, we divide the reference image in tiles
<CLICK>
Here we show only 4 tiles but we use many more in reality.

## Slide 11
Reference
Source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: For each tile we pick the most discriminative pixel, in other words, strong corners -- I will talk more about that in a couple of slides.
Instead of finding corners in the source image as well, for each corner in the reference,
<CLICK>
we initialize a search window around the location in the source image where we think the corner should be, and
<CLICK>
we refine our guess. We get our initial guess by using a pyramidal approach, propagating the information from the coarser layers.
Finally, we repeat this process for all the corners in the reference.

## Slide 12
Much brighter
or
much darker
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Notes: So how do we find these corners? Here is the intuition. Rather than looking at all the pixels in the tile, we look at discrete locations within each tile, and for each one of those
<CLICK>
we compute the average brightness in the four quadrant around it. Note that the average brightness can be very efficiently using integral images!
Now, aside from flat areas,
<CLICK>
these are all the possible configurations, where the green quadrants are much brighter or darker than the black quadrants.
It is easy to convince ourselves that
<CLICK>
the first two rows are discriminative, while the last one, essentially edges,
<CLICK>
are not because pixels moving along an edge won’t change their appearance.

## Slide 13
B2
B1
B3
B4
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: To be a little more formal, for each of these discrete locations,
<CLICK>
we define a measure of “cornerness” C, as the maximum difference between the average brightness in any two patches.
This measure could be high for edges as well, so we require that
<CLICK>
The minimum difference between any two adjacent quadrants be above threshold.
Among the discrete locations we analyze for each patch, we retain the one with the highest cornerness.

## Slide 14
Reference
Source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: So now we have a bunch of corners in both images as well as their correspondences. Note that this is a toy example, so you’ll have to use your imagination to picture the underlying texture that makes these points into good corners.
If we want to propagate the flow at these locations, we need to first make sure they are good matches!

## Slide 15
Reference
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: In particular, looking at these to images
<FLIP BACK AN FORTH>

## Slide 16
Source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: In particular, looking at these to images
<FLIP BACK AN FORTH>

## Slide 17
Reference
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: …we want to remove non-rigid matches such as these….
<FLIP BACK AN FORTH>

## Slide 18
Source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: …we want to remove non-rigid matches such as these….
<FLIP BACK AN FORTH>

## Slide 19
Reference
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: …and wrong matches such as these….
<FLIP BACK AN FORTH>

## Slide 20
Source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: …and wrong matches such as these….
<FLIP BACK AN FORTH>

## Slide 21
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: Our intuition is that “good” corners should be consistent with a homography. However, we don’t want to force that all the corners across the whole image be consistent with the same homography!

## Slide 22
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: We start by picking a random set of 4 points and fit a homography to them.

## Slide 23
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: We go look at the inliers and we see that they are very few. This could mean that they are not good matches, or that it simply wasn’t a good sample.

## Slide 24
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: So we move on, and we go back to the original candidates.

## Slide 25
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: We pick a new set of points,

## Slide 26
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: And this time the homography they induce has a large support. We like these matches
<CLICK>

## Slide 27
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: so we save their indexes and iterate…

## Slide 28
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: We then go back to the original set,

## Slide 29
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: Pick four other points,

## Slide 30
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: …and compute the homography and inliers. Once again, there is a large number of inliers, which suggests that each of them is a good match. So we save the indexes of the corners we found, and…

## Slide 31
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: … add them to the current set of indexes of good corners

## Slide 32
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference
Source
Notes: Finally we iterate the process until are reasonably sure that we found all the good corners.
Now that we know that we can trust these matches, we can propagate the information to all of the pixels.

## Slide 33
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Reference’s Luma
Sparse flow
Notes: Here is an intuition of how we do it. Recall that having the matches at sparse locations is equivalent to having the optical flow between the two images at those locations. Once again, imagine that there is some texture that justifies the fact that these points are corners.
<CLICK>
We can then cross-bilateral filter the two flow components, horizontal and vertical, using the luma of the reference image as a guide.
<CLICK>

## Slide 34
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: The idea is that when we propagate the flow we want to avoid propagating over strong boundaries: a pixel on one side of the boundary should only be affected by corners on the same side of the boundary.

## Slide 35
Reference
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: Once we have the flow at every pixel, we can warp the source image to match the appearance of the reference…
Here is a pair of images
<FLIP BACK AN FORTH>
You can see that there is a fairly large displacement, for a burst of images.

## Slide 36
Source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: Once we have the flow at every pixel, we can warp the source image to match the appearance of the reference…
Here is a pair of images
<FLIP BACK AN FORTH>
You can see that there is a fairly large displacement, for a burst of images.

## Slide 37
Reference
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: And this is the result after propagating the flow and warping…
<FLIP BACK AN FORTH>

## Slide 38
Warped source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: And this is the result after propagating the flow and warping…
<FLIP BACK AN FORTH>

## Slide 39
Warped source
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: The registration is pretty good, but actually this is a failure case for our algorithm, as you can see if you look carefully at these regions
<CLICK>
We account for these cases with the last step of our algorithm, which is an error-tolerant version of the Exposure fusion algorithm by Mertens et al.

## Slide 40
Corners and matches
Filter matches
Sparse-to-dense warp
Error-tolerant fusion
Notes: Specifically the original exposure fusion algorithm combines the images by using three weights and a pyramidal scheme. The weights account for color saturation, contrast, and correct exposure.
<CLICK>
We add a fourth weight to account for the local quality of the registration. Because we want something robust to changes in exposure and easy to compute we use the structural similarity index, SSIM.
Note that SSIM essentially requires computing five Gaussians on the image, which can be done in an extremely efficient way on GPU.
<CLICK>
Now those artifacts are gone.

## Slide 41: Performance
Notes: Now that I’ve given you an overview of our system let me convince you that it actually is very efficient and produces good quality results.

## Slide 42: Execution time for a pair of 5MP images
Notes: This is a break down of the timings for a pair of 5MP images. Remember that those “high-quality methods” took minutes on much smaller images, and note that we take less than 700ms on a mobile device! Granted it’s a powerful NVIDIA tablet, but it’s still a mobile device! 

## Slide 43
Quality
Speed
Rigid registration
(Ward ‘03,
Tomaszewska and Mantiuk ‘07, …)
Rejection methods
(Gallo ‘09,
Zhang and Cham ‘12,
Oh et al. ‘15 …)
Flow-based methods
(Zimmer et al. ‘11,
Zhang and Cham ‘12,…)
Related work
Minutes
Seconds
Milliseconds
No artifacts
Parallax
and
motion artifacts
Motion artifacts
or
reduced dynamic range
Accelerated patch-based
(Bao et al. ‘14)
Fully non-rigid registration
(Hu et al. ‘12, Sen et al. ‘12,
Hu et al. ‘13)
Notes: In fact, going back to the taxonomy I showed before, we can compare with the “best” and the “fastest” methods.
<CLICK>

## Slide 44
Quality
Speed
Related work
Minutes
Seconds
Milliseconds
No artifacts
Parallax
and
motion artifacts
Motion artifacts
or
reduced dynamic range
Accelerated patch-based
(Bao et al. ‘14)
Fully non-rigid registration
(Hu et al. ‘12, Sen et al. ‘12,
Hu et al. ‘13)
(VGA resolution)
Notes: And here, for a pair of VGA images, we can see that our algorithm is several times faster than the competitors.
More importantly, if we use larger images,
<CLICK>

## Slide 45
Quality
Speed
Related work
Minutes
Seconds
Milliseconds
No artifacts
Parallax
and
motion artifacts
Motion artifacts
or
reduced dynamic range
Accelerated patch-based
(Bao et al. ‘14)
Fully non-rigid registration
(Hu et al. ‘12, Sen et al. ‘12,
Hu et al. ‘13)
(5MP resolution)
Notes: We can’t even compare against Sen et al. or Hu et al. and the comparison against Bao et al.. Shows an 11x speedup.

## Slide 46
What about visually?
Ours
Bao et al.’s
(2.5MP)
Notes: But what about visual quality?
We saw that our method works as well or better than the method by Bao et al.’s as you can appreciate from the artifacts in the warped source produced by their method!

## Slide 47: To sum up…
A fast registration algorithm >11x faster than the fastest published method
We propose to use a sparse-to-dense approach
In particular we propose:
  A fast and robust matcher (works better than the state of the art in dark regions)
  A fast method to filter matches between two images
  An error-tolerant image fusion method
Contributions

## Slide 48: More results
Reference
Source
Warped source
HDR
Notes: And now I will take questions while I show some more results…

## Slide 49: More results
Naïve fusion
Our result
Notes: And now I will take questions while I show some more results…

## Slide 50: More results
Reference
Source
Warped source
HDR
Notes: And now I will take questions while I show some more results…

## Slide 51: More results
Naïve fusion
Our result
Notes: And now I will take questions while I show some more results…

## Slide 52: More results
Reference
Source
Warped source
HDR
Notes: And now I will take questions while I show some more results…

## Slide 53: More results
Naïve fusion
Our result
Notes: And now I will take questions while I show some more results…

## Slide 54: That’s all.